## Slide 1
IOT-BASED SMART TUNNEL
MONITORING SYSTEM
PROGRESS REPORT PRESENTATION
Student A : Ahmad Syalimin bin Mohd Amin (Student A)
Student B : Muhammad Shafwan bin Anis (Student B)
Student C : Low Ying Chian (Student C)
YouTube Video link :
https://youtu.be/9VrG6voz_LQ?si=4Ow9gxQraEuQ9wtq

## Slide 2
Background
  Tunnels in urban areas are vulnerable to flooding and hazardous conditions during heavy rainfall.
  Sudden water rise in tunnels can cause accidents, vehicle damage, and traffic disruption.
  Conventional tunnel monitoring systems often rely on manual observation or delayed response.
  Sensor-based automation enables real-time monitoring and faster safety actions.
  This project introduces a Smart Tunnel System using sensors and an automatic gate mechanism.
Problem Statement
  Tunnel conditions can change rapidly due to rainfall and rising water levels.
  Manual monitoring may not respond fast enough during emergency situations.
  Vehicles may still enter tunnels during unsafe conditions, increasing accident risk.
  There is a need for an automated tunnel safety system that can detect danger and respond immediately.
Objective
  To monitor tunnel environmental conditions using multiple sensors.
  To determine SAFE or DANGER status based on predefined thresholds.
  To control a servo motor acting as an automatic tunnel gate.
  To provide visual safety indication using red and green LEDs.

## Slide 3
STUDENT A
Hardware & Sensor Integra􀆟on
Ahmad Syalimin bin Mohamad Amin
231061451

## Slide 4
Component | Function
Ultrasonic sensor | Dam Monitor (Early Warning). Measures water level at the dam. If the dam is too full, it alerts the tunnel of flood risk.
Water level sensor | Tunnel Flood Detector. Detects if water is actually flowing inside the tunnel right now.
Rain sensor | Rain Detector. Detects if it is raining heavily outside the tunnel.
Esp 32 | Main control. It reads all sensors and decides if the tunnel is Safe or Dangerous.
Red and green LED | Red Led as STOP Signal Green Led as SAFE Signal .
Servo motor | Automatic tunnel gate actuator
Component

## Slide 5
Circuit Diagram

## Slide 6
Flow process
YES
YES
YES
NO
NO
NO

## Slide 7
Block Diagram

## Slide 8
Problem:
Sensor readings fluctuate and are not consistent during operation.
Solution:
Use Vin for the ultrasonic sensor and 3v3 for other sensor
Problems faced
Problem:
Analog sensor values are affected by noise, causing unstable ADC readings.
Solution:
Reduce wire length between sensors and ESP32

## Slide 9
STUDENT B
IoT Communication & Dashboard
Muhammad Shafwan bin Anis
231061512

## Slide 10
IOT Architecture

## Slide 11
IOT Architecture
Perception Layer
  Sensors: HC-SR04 (River Distance), Rain Sensor (Intensity), Water Level Sensor (Overflow detection).
  Processing: ESP32 DevKit V1 aggregates sensor data & executes local safety logic.
  Actuators: SG90 Servo (Simulated Gate) + Red/Green LEDs (Visual Status Indicators).
  Output: Physical environmental readings converted into digital JSON telemetry.
Network Layer
  Connectivity: Wi-Fi via ESP32 (IEEE 802.11 b/g/n @ 2.4GHz) for Internet access.
  Protocol: MQTT (Lightweight Pub/Sub) selected for low latency & reliability.
  Broker: HiveMQ Cloud acts as the central router between Edge & Cloud.
  Topic: Data published to monash/studentB/tunnel_data for specific routing.
  Output: Telemetry packetized into JSON format for efficient transmission.
Middleware Layer
  Processing: Python Gateway subscribes to MQTT topics & parses JSON telemetry.
  Safety Logic: Real-time evaluation of sensor thresholds (e.g., Water > 1000 = Danger).
  Storage: InfluxDB (Time-Series) optimized for high-speed sensor data ingestion.
  Alerting: Triggers Telegram Bot API (HTTPS) immediately upon critical event detection.
  Output: Structured data streams ready for dashboard visualization.
Application Layer
  Visualization: Grafana Dashboard enables real-time monitoring of River, Rain & Flood status.
  Alert System: Telegram Mobile App receives instant push notifications for critical "Flood" warnings.
  Analytics: Historical data trends visualized to track river behavior over time.
  User Interface: Simple "Red/Green" safety status for immediate decision-making by operators.
  Output: Actionable insights for disaster response & tunnel management.

## Slide 12
System Analysis & Specifications
SYSTEM ANALYSIS & SPECIFICATIONS
IEEE STANDARDS & HARDWARE SPECS
PROTOCOL COMPARISON: ADVANTAGES VS. LIMITATIONS
CLOUD SERVICES OVERVIEW & LIMITATIONS
  Wi-Fi Standard: IEEE 802.11 b/g/n (2.4 GHz Band).
  Transfer Rate: Up to 150 Mbps (Ensures fast JSON transmission).
  Power Consumption: ESP32 consumes ~80mA (Idle) to ~240mA (Tx).
  Range Limit: ~50m (Indoor) / ~100m (Outdoor), dependent on router placement.
  MQTT (Advantages): Lightweight header (2 bytes) & "Keep-Alive" function reduces network overhead.
  MQTT (Limitations): Centralized Broker dependency (Single Point of Failure).
  Wi-Fi (Limitations): Higher power drain compared to LoRaWAN; signal attenuation through concrete walls.
  Security: TLS/SSL encryption enabled for Telegram & HiveMQ to prevent Man-in-the-Middle attacks.
  HiveMQ Broker: Acts as the real-time message router.
  Limitation: Free Tier capped at 10GB bandwidth/month.
  InfluxDB: Optimized for high-speed Time-Series write operations.
  Limitation: Data retention policy restricted to 30 days (Free Tier).
  Grafana: Visualizes 5-second interval updates for Trend Analysis.

## Slide 13
INFLUXDB INTERFACE
GRAFANA INTERFACE

## Slide 14
Data Analytics
STUDENT C
Low Ying Chian
231062387

## Slide 15
Data Analytics
Analytics Approach
  Descriptive: Monthly water level patterns
  Diagnostic: Rain–water level relationship
  Predictive: Flood probability by month
  Prescriptive: Risk-based operational actions
Key Findings
  Water level peaks during monsoon season (Nov–Dec)
  Strong positive correlation between rainfall and water level
  Flood probability exceeds 70% during peak months
Risk Classification Logic
  Safe: Normal operation
  Alert: Increased monitoring
  Danger: Tunnel closure & pump activation
Impact & SDG 11 Contribution
  Early flood warning
  Improved tunnel safety
  Enhanced urban resilience

## Slide 16
Telegram
Smart Tunnel Sensor Thresholds
1️⃣ Ultrasonic Sensor
🟢 Safe: ≥ 15
🟡 Alert: 10 – 14
🔴 Danger: < 10
2️⃣ Water Level Sensor
🟢 Safe: < 600
🟡 Alert: 600 – 999
🔴 Danger: ≥ 1000
3️⃣ Rain Sensor
🟢 Dry / Safe: 3501 – 4100
🟡 Moderate Rain / Alert: 3000 – 3500
🔴 Heavy Rain / Danger: 0 – 2999

## Slide 17
Thank You

## Slide 18
Backup Slide

## Slide 19
Experiment 1 : Calculate latency
Average latency : 1.2248 s

## Slide 20
Experiment 2 : Calculate latency Variance from distance
Average latency : 1.2209 s
Scenario 1: Besides the laptop

## Slide 21
Experiment 2 : Calculate latency Variance from distance
Average latency : 1.6027 s
Scenario 2 : ~1 m from the source

## Slide 22
Experiment 2 : Calculate latency Variance from distance
Average latency : 1.1908 s
Scenario 3 : At the room

## Slide 23
Experiment 3 : Calculate WiFi
---> Then try to On & Off the WiFi
Result :
Python Bridge can connect
ESP 32 Could not connect

## Slide 24
Experiment 3 : Calculate WiFi
Improvement : Add auto connect
connect_mqtt()
Result : Pass